## Slide 1: (DRAFT) Final Presentation
Naravich Chutisilp, MSc. CS EPFL
Supervisor Edelman R. Elazer, M.D., Ph.D.
Supervisor Maria Brbic, Ph.D.
Daily Supervisor Karim Kadry, Ph.D. candidate

## Slide 2: Executive Summary
nnU-Net is the best performing framework for Calcium segmentation
Pre-training nnU-Net with larger annotated OCT data significantly improves 3D segmentation
3D segmentation better retains its continuity after post-processing than 2D counterpart, which is beneficial in tasks such as diffusion model
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
CNN-based is the most suitable algorithm in our setting
This may due to the nature of calcium which is monolithic and is situated locally in the image which does not require global context to help identify where it is.

## Slide 3: Executive Summary (conT’)
Fine-tuning transformer-based models is not as good as CNN-based nnU-Net
Unimodal SSL algorithms are not outperforming the best nnU-Net models
Multi-modal SSL on co-registered OCT images is as effective as pre-training the model with a larger annotated OCT while potentially requires lower cost of obtaining the data
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 4: Algorithms
CNN-based supervised learning segmentation – nnU-Net
Transformer-based supervised learning segmentation - SegFormer
Transformer-based medical supervised learning – SuPReM
Unimodal self-supervised learning – Genesis
Unimodal self-supervised learning – V-JEPA
Multi-modal self-supervised learning - CLIP
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 5: Nn U-Net
Self-configuring U-Net
Robust training pipeline
Work well on small to medium sized medical dataset
nnU-Net framework
U-Net architecture
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 6: nn U-Net
2D is performing better than 3D segmentation
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 7: nn U-Net
Patch size significantly affects 3D segmentation performance
Pre-training models with Lumen and Wall OCT (LaW OCT) dataset significantly improves 3D segmentation
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
x,y,z rather than z,x,y
Dice score

## Slide 8: nn U-Net
3D segmentation has a better trade off between performance vs. continuity
Continuity is vital in conditional 3D image generation with diffusion model
  Inverse of average change
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 9: SegFormer
Transformer-based segmentation model
Explicitly utilize multi-resolution features similar to CNN-based counterpart, U-Net
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 10: SegFormEr
SegFormer (ADE60k)’s performance is significantly lower than 3D nnU-Net
Transformer model is proven to perform better when there are enough data (i.e. more parameters require more data to learn good representations)
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 11: SuPrem
Supervised Pre-training Model (SuPreM)
Pre-train multiple models with 9,262 CT volumes with 25 organ annotation (AbdomenAtlas 1.1 dataset)
However, only pre-trained models on 2,100 CT volumes are available
Swin UNETR is their best performing model
Thus, SuPreM Swin UNETR is fine-tuned on Calcium OCT segmentation
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 12: SuPrem - Swin UNETR
Transformer-based segmentation model
Utilize CNN-based decoder instead of MLPs in SegFormer
Explicitly utilize multi-resolution features
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 13: SuPrem - Swin UNETR
SuPreM pre-training is significantly more effective than originally proposed SSL pre-training and training the model from scratch
SuPreM pre-training is significantly less effective than nnU-Net
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 14: Genesis
Reconstructive pre-text tasks to learn visual representations
U-Net as their backbone architecture
Thus, nnU-Net is used
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 15: Genesis
Genesis pre-training can successfully reconstruct distorted coronary artery OCT images
Genesis output on validation set
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 16: Genesis
Genesis does not improve the 3D segmentation of nnU-Net
Representation learned from Genesis might not be useful for identifying calcium, and it might also be an overhead for the model to re-learn how the calcium look
Initial epoch prediction (validation)
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Genesis pre-text task may not be suitable for the nature of calcium which is monolithic. Distorting the calcium area may not result in the area visually being different, so this task might not be useful for calcium segmentation.
Representations learned from Genesis pre-training could be useful in segmenting objects that has clear boundary and textured like how it performs well in segmenting organs in CT images
Dice score

## Slide 17: V-JEPA
Efficient generative pre-text task to learn visual representations
Use Vision Transformer (ViT) as their backbone
Pre-trained on 2 million videos
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 18: V-JEPA – Decoder Head
ViT does not have a segmentation decoder head
It is open-ended which decoder head would fit the best
Linear batch normalization is used in DINOv2 and RADIO
Attentive decoder is experimented following V-JEPA’s attentive classification
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 19: V-JEPA – Decoder Head
Multi-feature is inspired by SegFormer’s decoder head
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 20: V-JEPA – Decoder Head
Attentive decoder is slightly better and their counterparts
It could be slightly improved with more augmentation and data sampling
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 21: V-JEPA
V-JEPA performs significantly lower than nnU-Net
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 22: V-JEPA
V-JEPA pre-training significantly improves segmentation with ViT
However, pre-training V-JEPA on our unannotated OCT images is not significantly beneficial
Amount of unannotated data for pre-training may have a crucial role (2M vs. 300)
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Even though masking the OCT images for pre-training should provide the ViT more relevant information to learn representations from, 300 volumes might not be enough for ViT to learn from, and masking strategy may need to be revised as a lot of the area in OCT are lumen, probing head and background which are irrelevant for calcium segmentation
Dice score

## Slide 23: CLIP
Contrastive pre-text task to align representation of multi-modal data
Pre-IVL
Post-IVL
Pre-IVL
Post-IVL
Mariia’s co-registered data
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 24: CLIP
Pre-training does not converge when following the original paper’s naively
Pre-IVL
Post-IVL
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 25: CLIP
Image encoder must be shared among different image modalities for CLIP pre-training to converge
Pre-IVL and Post-IVL share similar morphology, so it is logical to share an encoder to accelerate the convergence
It should be noted that separate encoder could be beneficial when co-registered Pre-IVL and Post-Stent is used
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP

## Slide 26: CLIP
CLIP significantly improves 3D nnU-Net segmentation
Using co-register multi-modal datasets with CLIP can yield a comparable improvement as fully annotated data lumen and wall datasets
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 27: Conclusion
nnU-Net is the best performing model
LaW OCT pre-training is significantly beneficial for 3D nnU-Net
Transformer-based models require more data annotations and its ability to learn global context of images may not be beneficial to the nature of calcium who is monotonic and local
CLIP on co-registered data equally improve 3D nnU-Net while costing less in data acquisition
nnU-Net | SegFormer | SuPreM | Genesis | V-JEPA | CLIP
Dice score

## Slide 28: Discussion and observation
20 datapoints in lumen and wall segmentation might be enough
Dice score is not decreasing, but the “confident” (cross entropy loss) may be decreasing. It would be nice to plot the CELoss as well

## Slide 29: Discussion and observation
More data annotation would improve calcium segmentation

## Slide 30: Discussion and observation
Visually good features do not always lead to a higher performance in segmentation
Features from RADIO model
Features from 2D nnU-Net
Visual feature of the RADIO model can distinguish different morphology of the OCT image. However, calcium is not at semantic level, so this feature might not be beneficial for calcium segmentation.

## Slide 31: Discussion and observation
ViT
ViT (V-JEPA VideoMix2M)
Original image
Visually good features do not always lead to a higher performance in segmentation

## Slide 32: SSL Pre-training
A model can be successful with Genesis pre-text task
The same is not true for V-JEPA and CLIP
V-JPEA loss may not always converge, and the author does not address how
The nature of this pre-text task makes it more difficult to trace the issue

## Slide 33: SSL Pre-training (V-JEPA)
Epoch 0 Iteration 2
Epoch 67 Iteration 298
Epoch 99 Iteration 299
Epoch 207 Iteration 19
Epoch 299 Iteration 290
Epoch 299 Iteration 291
Epoch 299 Iteration 298

## Slide 34: SSL Pre-training (CLIP)
Validation logits (should look like identity matrix)
Input (same image)
Separate encoder and separate projector

## Slide 35: SSL Pre-training (CLIP)
Validation logits (should look like identity matrix)
Input (same image)
Separate encoder and shared projector

## Slide 36: SSL Pre-training (CLIP)
Validation logits (should look like identity matrix)
Input (Pre-IVL & Post-IVL)
Separate encoder and shared projector

## Slide 37: SSL Pre-training (CLIP)
Validation logits (should look like identity matrix)
Input (Pre-IVL & Post-IVL)
Shared encoder and shared projector (final design)